## Slide 1: NTP Sub-group NTP Time Stamp Proposal 10 October 2017

## Slide 2: Proposed NTP Time Stamp SFR
Maintaining Integrity in System Date/Time
[The following is an optional SFR]
  This is a selection-based SFR, to be included in the ST if “synchronise time with external time source” is selected within FPT_STM_EXT.1.2.
  This SFR is not applicable when NTP is being used between TOE components, as such communications would be implicitly covered by FPT_ITT.1.
  This SFR is not applicable if the TOE cannot be configured to operate as an NTP time recipient (client or peer), even if the TOE can operate as an NTP time source (server or peer) for non-TOE entities. Such communications could potentially be listed as a capability within FTP_ITC.1.
FCS_NTP_EXT.1 NTP Protocol
FCS_NTP_EXT.1.1 The TSF shall implement [selection: NTP v3 (RFC 1305), NTP v4 (RFC 5905)] NTP versions.
FCS_NTP_EXT.1.2 The TSF shall update its system time using [selection:
        Symmetric Cryptography [selection: SHA1, SHA224, SHA256, SHA384, SHA512, AES-CBC-128, AES-CBC-256] as the cryptographic algorithm(s);
        The TSF shall be capable of using [selection: IPsec, DTLS] to provide trusted communication between itself and an NTP time source.
        ].
FCS_NTP_EXT.1.3 The TSF shall not update NTP timestamp from broadcast addresses.
FCS_NTP_EXT.1.4 The TSF shall support configuration of at least three (3) NTP time sources.
  Application note: The TOE has to support configuration of at least 3 time sources though not mandate that the TOE is configured to always use at least 3 time sources.

## Slide 3: Proposed FMT_SMF.1 SFR Update
Update to FMT_SMF.1 to include functions if NTP is selected.
    Update list of management functions that may be selected as follows:
      [selection:
          Ability to configure audit behaviour;
          Ability to configure the list of TOE-provided services available before an entity is identified and authenticated, as specified in FIA_UIA_EXT.1;
          ….
          ….
          Ability to set the time which is used for time-stamps;
          Ability to configure NTP;
          Ability to configure the reference identifier for the peer;
          ….
          ….
        ].
Update the Application Note 23 as follows:
    The TOE must provide…
    The selection “Ability…
    The selection “Ability…
    The selection “Ability to configure NTP” shall be included in the ST if the TOE uses NTP for timestamp configuration. If selected, FCS_NTP_EXT.1 shall be included in the ST as well.

## Slide 4: Proposed NTP SFR AAs
Evaluation Activities
TSS
The evaluator shall examine the TSS to ensure it describes what approach the TOE uses to ensure the timestamp it receives from an NTP time server (or NTP peer) is from an authenticated source and the integrity of the time has been maintained.
The TOE may use multiple methods, as specified in the SFR, and the evaluator determines that each method selected in the ST is described in the TSS, including the algorithms and protocols used to ensure authenticity and integrity of the timestamp.
Guidance Documentation
The evaluator shall examine the guidance documentation to ensure it provides the administrator instructions on how to configure the multiple NTP servers for the TOE’s time source and how to configure the TOE to use the method(s) that are selected in the ST.
Each primary selection in the SFR contains selections that specify a cryptographic algorithm or cryptographic protocol. For each of these secondary selections made in the ST, the guidance documentation instructs the administrator how to configure the TOE to use the chosen option(s).

## Slide 5: Proposed NTP SFR AAs
Test
The version of NTP specified in the first selection will have to be verified it is supported by the TOE.
The cryptographic algorithms specified in the second selection of this SFR will have been specified in an FCS_COP SFR and tested in the accompanying Evaluation Activity for that SFR. Likewise the cryptographic protocol selected in the second selection of this SFR will have been specified in an FCS SFR and tested in the accompanying Evaluation Activity for that SFR.
The evaluator will perform the following test(s) to verify the TOE implements the selected option(s) correctly:
  Test 1: The evaluator shall configure an NTP server to use the NTP version selected by the ST Author to communicate with the NTP client, the TOE. The evaluator configures either the NTP server’s clock or the TOE’s clock such that the TOE will update its time when it receives a packet from the NTP server. The difference in time must be enough to force a step in time on the TOE and to be observable by examining the TOE’s system time before and after the event.
    The evaluator shall use a packet sniffer to capture the network traffic between the TOE and the NTP server. The evaluator uses the captured network traffic, to observe time change of the TOE and uses the TOE’s audit log to determine that the TOE accepted the NTP server’s timestamp update and that the appropriate method(s) and option(s) were used to transmit the packet. The evaluator shall also confirm that the TOE does not synchronize to any other time sources.
  Test 2: The evaluator shall configure NTP servers to support periodic time updates to broadcast addresses. The evaluator shall confirm the TOE is configured to not accept/receive/process broadcast NTP packets.

## Slide 6: Allocation of Requirements in Distributed TOEs
Requirement | Description | Distributed TOE SFR Allocation
FCS_NTP_EXT.1 | NTP Protocol | Other

## Slide 7: Background Information
Autokey Consideration:
There is published information on the issues using Autokey. The published information details the weaknesses in Autokey and the ease at which the timestamp data can be modified and passed along with no indication the data has been tampered.
Including Autokey as a means to authenticate the integrity of the time source provides a false sense of security that the timestamp being received is authentic and unaltered.
  Reference - https://www.ietf.org/proceedings/83/slides/slides-83-tictoc-1.pdf . In summary the paper shows that an attack can be preformed fast enough that the autokey session can be hacked in real time, crafting and sending a response well before the client times out waiting for the real (legitimate) time data.
  Reference - https://www.eecis.udel.edu/~mills/security.html where it is acknowledged "the cookie size of 4 octets is way too small"
SSH and TLS Consideration:
SSH and TLS were not included as protocols to secure the connection with the NTP server as neither support datagram protocols
Algorithm Consideration:
The focus of the algorithms was based on NDcPPv2.0. Not all algorithms in the FCS_COP* align well with NTP. AES CBC mode was chosen because it is well defined and well understood symmetric ciphers. CTR is really no different than CBC, except for seed and GCM is complex. Signatures not required to provide the integrity of the time source and HMAC usage is associated with Autokey and other interoperability issues.
NTP mode Consideration:
Broadcast is not allowed given all nodes on the network see all traffic and offers a potential for hacking. At this time there is no requirement not to use any of the other modes and they are more controlled, for example multicast the administrator has to subscribe to receive information, therefore the entity is known.

## Slide 8: Thank you