## Slide 1: NTP Sub-group 2 June2017

## Slide 2: Where We Are
We have defined and formatted the SFRs to support NTPv4 as a reliable time source.
Assurance Activities have been drafted

## Slide 3: Proposed SFR Time Stamp
Maintaining Integrity in System Date/Time
[The following is an optional SFR]
FPT_STM_EXT.1 Authentication of System Time updates
FPT_STM_EXT.1 The TSF shall update its system time using [selection:
    • Network Time Protocol version 4 (NTPv4) as specified in RFC 5905, using Symmetric Cryptography [selection: SHA1, HMAC-SHA2, AES-CBC-256] as the cryptographic algorithm(s);
    • Network Time Protocol version 4 (NTPv4) as specified in RFC 5905, using Autokey as specified in RFC 5906 using the following identity schemes: [selection: trusted certificate (TC), a modified Schnorr algorithm (IFF - Identify Friend or Foe), a modified Guillou-Quisquater (GQ) algorithm, a modified Mu-Varadharajan (MV) algorithm].
    • The TSF shall be capable of using [selection: IPsec, DTLS] to provide trusted communication between itself and an NTP server
]
Application Note 1
  Use of this SFR indicates the TOE provides an NTP client that implements NTPv4 and complies with the corresponding standard. While RFC 5906 identifies 5 schemes available in the reference implementation, there are only three schemes that use a cryptographically strong challenge-response exchange: (1) a modified Schnorr algorithm (IFF aka Identify Friendly or Foe), (2) a modified Guillou-Quisquater (GQ) algorithm, and (3) a modified Mu-Varadharajan (MV) algorithm. The Trusted Certificate (TC) uses a certificate trail and is not considered an identity scheme according to RFC 5906. The Private Certificate scheme described in RFC 5906 is not intended to be used in an operational environment.
  It is noted that for this requirement that “NTP server” also includes an entity acting as an NTP peer.

## Slide 4: Proposed SFR Time Stamp AAs
Evaluation Activities
TSS
The evaluator shall examine the TSS to ensure it describes what approach the TOE uses to ensure the timestamp it receives from an NTP server (or NTP peer) is from an authenticated source and the integrity of the time has been maintained. The TOE may use multiple methods, as specified in the SFR, and the evaluator determines that each method selected in the ST is described in the TSS, including the algorithms and protocols used to ensure authenticity and integrity of the timestamp.
Guidance Documentation
The evaluator shall examine the guidance documentation to ensure it provides the administrator instructions on how to configure the TOE to use the method(s) that are selected in the ST. Each primary selection in the SFR contains selections that specify a cryptographic algorithm, an identity scheme, or cryptographic protocol. For each of these secondary selections made in the ST, the guidance documentation instructs the administrator how to configure the TOE to use the chosen option(s).
Test
The cryptographic algorithms specified in the first selection of this SFR will have been specified in an FCS_COP SFR and tested in the accompanying Evaluation Activity for that SFR. Likewise the cryptographic protocol selected in the last selection of this SFR will have been specified in an FCS SFR and tested in the accompanying EA for that SFR.
The evaluator will perform the following test(s) for each of the method(s) selected, and each of the option(s) within a method, to verify the TOE implements the selected method(s) and option(s) correctly:
  a) Test 1: The evaluator shall configure an NTP server to use the method selected by the ST Author to communicate with the NTP client – the TOE. The evaluator configures either the NTP server’s clock or the TOE’s clock such that the TOE will update its time when it receives a packet from the NTP server – the difference in time must be enough to force a step in time, and to be observable by examining the TOE’s system time before and after the event. The evaluator shall use a packet sniffer to capture the network traffic between the TOE and the NTP server. The evaluator uses the captured network traffic, the observed time change of the TOE, and the TOE’s audit log to determine that the TOE accepted the NTP server’s timestamp update and that the appropriate method and option was used to transmit the packet.

## Slide 5: Feedback - SFR
Autokey:
There is published information on the issues using Autokey
SSH and TLS:
SSH and TLS were not included as protocols to secure the connection with the NTP server as neither support datagram protocols
NTPv3:
NTPv3 should also be included for use with the same methods to authenticate the integrity of the timesource/timestamp
SHA2:
Add SHA2 alogrithms

## Slide 6: Feedback - AAs
Guidance:
"Each primary selection in the SFR contains selections that specify a cryptographic algorithm, an identity scheme, or cryptographic protocol. For each of these secondary selections made in the ST, the guidance documentation instructs the administrator how to configure the TOE to use the chosen option(s)."
I understand that you want clear guidance instructions for each selected method. However, this overly specific language will lead to a lot of unnecessary grief for the labs. For example, rarely specifics of NTP are user-configurable. However this evaluation activity written with fully configurable implementation in mind. Instead, I recommend replacing quoted section with the following:
  "For all administrator-configurable NTP parameters, the guidance documentation must instruct the administrator how to configure the TOE and document default settings."
Test:
" a) The evaluator uses the captured network traffic, the observed time change of the TOE, and the TOE’s audit log to determine that the TOE accepted the NTP server’s timestamp update and that the appropriate method and option was used to transmit the packet."
I don't believe this is adequate to ensure correct functionality. We should add negative test cases to make sure the TOE performs cryptographic checks. That is, "default to accept everything" flawed implementation would likely remain undetected by testing activities as written.
I think we need conditional cases for each selection:
--- good signature, bad signature for symmetric cryptography selection
--- good signature trusted cert, bad signature trusted cert, untrusted cert good signature for autokey selection
--- inspect protocol handshake and confirm secure channel established, interrupt/timeour channel and make sure it is correctly renegotiated/resumed for secure channel selection

## Slide 7: Next Steps
Team review Autokey evidence – Terrie will send to the group as soon as received
Make changes based on the Autokey evidence
Update SFR and AAs, include rationale for the changes
Team review updates/approve
Submit to ND iTC
Provide a copy to NIAP for consideration to change PPs/EPs that include Autokey – note this is conditional based on review of Autokey evidence and changes made by this Subgroup

## Slide 8: Thank you