## Slide 1: NTP Sub-group 16 June2017

## Slide 2: Proposed Solution
Remove Autokey as a selection to authenticate the integrity of the time source
Keep NTPv4, adding NTPv3 and changing to a selection
Add SHA2 algorithms

## Slide 3: Proposed SFR Time Stamp
Maintaining Integrity in System Date/Time
[The following is an optional SFR]
FCS_NTP_EXT.1 NTP Protocol
FCS_NTP_EXT.1 The TSF shall implement [selection: NTP v3 (RFC 1305), NTP v4 (RFC 5905)] and reject all other NTP versions.
FCS_NTP_EXT.2 The TSF shall update its system time using [selection:
        Symmetric Cryptography [selection: SHA1, SHA224, SHA256, SHA384, SHA512, AES-CBC-128, AES-CBC-256] as the cryptographic algorithm(s);
        The TSF shall be capable of using [selection: IPsec, DTLS] to provide trusted communication between itself and an NTP server
].
Application Note 1
  Use of this SFR indicates the TOE provides an NTP client that implements either NTPv3 or NTPv4 and complies with the corresponding standard.
  It is noted that for this requirement that “NTP server” also includes an entity acting as an NTP peer.

## Slide 4: Proposed SFR Time Stamp AAs
Evaluation Activities
TSS
The evaluator shall examine the TSS to ensure it describes what approach the TOE uses to ensure the timestamp it receives from an NTP server (or NTP peer) is from an authenticated source and the integrity of the time has been maintained. The TOE may use multiple methods, as specified in the SFR, and the evaluator determines that each method selected in the ST is described in the TSS, including the algorithms and protocols used to ensure authenticity and integrity of the timestamp.
Guidance Documentation
The evaluator shall examine the guidance documentation to ensure it provides the administrator instructions on how to configure the TOE to use the method(s) that are selected in the ST. Each primary selection in the SFR contains selections that specify a cryptographic algorithm, an identity scheme, or cryptographic protocol. For each of these secondary selections made in the ST, the guidance documentation instructs the administrator how to configure the TOE to use the chosen option(s).
Test
The version of NTP specified in the first selection will have to be verified it is supported by the TOE.
The cryptographic algorithms specified in the second selection of this SFR will have been specified in an FCS_COP SFR and tested in the accompanying Evaluation Activity for that SFR. Likewise the cryptographic protocol selected in the second selection of this SFR will have been specified in an FCS SFR and tested in the accompanying EA for that SFR.
The evaluator will perform the following test(s) to verify the TOE implements the selected option(s) correctly:
  a) Test 1: The evaluator shall configure an NTP server to use the NTP version selected by the ST Author to communicate with the NTP client – the TOE. The evaluator configures either the NTP server’s clock or the TOE’s clock such that the TOE will update its time when it receives a packet from the NTP server – the difference in time must be enough to force a step in time, and to be observable by examining the TOE’s system time before and after the event. The evaluator shall use a packet sniffer to capture the network traffic between the TOE and the NTP server. The evaluator uses the captured network traffic, the observed time change of the TOE, and the TOE’s audit log to determine that the TOE accepted the NTP server’s timestamp update and that the appropriate method and option was used to transmit the packet.

## Slide 5: Feedback – original SFR
Autokey:
There is published information on the issues using Autokey. The published information details the weaknesses in Autokey and the ease at which the timestamp data can be modified and passed along with no indication the data has been tampered.
Including Autokey as a means to authenticate the integrity of the time source provides a false sense of security that the timestamp being received is authentic and unaltered.
  Reference - https://www.ietf.org/proceedings/83/slides/slides-83-tictoc-1.pdf . In summary the paper shows that an attack can be preformed fast enough that the autokey session can be hacked in real time, crafting and sending a response well before the client times out waiting for the real (legitimate) time data.
SSH and TLS:
SSH and TLS were not included as protocols to secure the connection with the NTP server as neither support datagram protocols
NTPv3:
NTPv3 should also be included for use with the same methods to authenticate the integrity of the timesource/timestamp
SHA2:
Add SHA2 algorithms

## Slide 6: Feedback - AAs
Guidance:
"Each primary selection in the SFR contains selections that specify a cryptographic algorithm or cryptographic protocol. For each of these secondary selections made in the ST, the guidance documentation instructs the administrator how to configure the TOE to use the chosen option(s)."
I understand that you want clear guidance instructions for each selected method. However, this overly specific language will lead to a lot of unnecessary grief for the labs. For example, rarely specifics of NTP are user-configurable. However this evaluation activity written with fully configurable implementation in mind. Instead, I recommend replacing quoted section with the following:
  "For all administrator-configurable NTP parameters, the guidance documentation must instruct the administrator how to configure the TOE and document default settings."
Test:
" a) The evaluator uses the captured network traffic, the observed time change of the TOE, and the TOE’s audit log to determine that the TOE accepted the NTP server’s timestamp update and that the appropriate option was used to transmit the packet."
I don't believe this is adequate to ensure correct functionality. We should add negative test cases to make sure the TOE performs cryptographic checks. That is, "default to accept everything" flawed implementation would likely remain undetected by testing activities as written.
I think we need conditional cases for each selection:
--- good signature, bad signature for symmetric cryptography selection
--- inspect protocol handshake and confirm secure channel established, interrupt/timeout channel and make sure it is correctly renegotiated/resumed for secure channel selection

## Slide 7: Next Steps
Team members provide comments on proposed solution and send to Terrie by 23 June 2017
[Terrie] Consolidate write-ups and send to the Team
Review write-up at next meeting, make necessary changes, finalize and submit to ND iTC
  Provide a copy to NIAP for consideration to change PPs/EPs that include Autokey
Next meeting is 10:00am (est) 30 June 2017….however Terrie will be on PTO so either someone (Andy???) can run the meeting so we can continue to move forward or we will just meetup at the next scheduled meeting on 14 July 2017.

## Slide 8: Thank you