## Slide 1: NTP Sub-group 17 July 2017

## Slide 2: Proposed SFR Time Stamp
Maintaining Integrity in System Date/Time
[The following is an optional SFR]
FCS_NTP_EXT.1 NTP Protocol
FCS_NTP_EXT.1.1 The TSF shall implement [selection: NTP v3 (RFC 1305), NTP v4 (RFC 5905)] and reject all other NTP versions.
FCS_NTP_EXT.1.2 The TSF shall update its system time using [selection:
        Symmetric Cryptography [selection: SHA1, SHA224, SHA256, SHA384, SHA512, AES-CBC-128, AES-CBC-256] as the cryptographic algorithm(s);
        The TSF shall be capable of using [selection: IPsec, DTLS] to provide trusted communication between itself and an NTP time source.
        ].
FCS_NTP_EXT.1.3 The TSF shall support configuration of at least three (3) NTP time sources.

## Slide 3: Proposed FMT_SMF.1 SFR Update
Update to FMT_SMF.1 to include functions if NTP is selected.
    Update list of management functions that may be selected as follows:
      [selection:
          Ability to configure audit behaviour;
          Ability to configure the list of TOE-provided services available before an entity is identified and authenticated, as specified in FIA_UIA_EXT.1;
          ….
          ….
          Ability to set the time which is used for time-stamps;
          Ability to configure NTP time source;
          Ability to configure the reference identifier for the peer;
          ….
          ….
        ].
Update the Application Note 23 as follows:
    The TOE must provide…
    The selection “Ability…
    The selection “Ability…
    The selection “Ability to configure NTP time source” shall be included in the ST if the TOE uses NTP for timestamp configuration. If selected, FCS_NTP_EXT.1 shall be included in the ST as well.

## Slide 4: Proposed SFR NTP Time Source AAs
Evaluation Activities
TSS
The evaluator shall examine the TSS to ensure it describes what approach the TOE uses to ensure the timestamp it receives from an NTP time server (or NTP peer) is from an authenticated source and the integrity of the time has been maintained. The TOE may use multiple methods, as specified in the SFR, and the evaluator determines that each method selected in the ST is described in the TSS, including the algorithms and protocols used to ensure authenticity and integrity of the timestamp.
Guidance Documentation
The evaluator shall examine the guidance documentation to ensure it provides the administrator instructions on how to configure the TOE to use the method(s) that are selected in the ST. Each primary selection in the SFR contains selections that specify a cryptographic algorithm, an identity scheme, or cryptographic protocol. For each of these secondary selections made in the ST, the guidance documentation instructs the administrator how to configure the TOE to use the chosen option(s).
Test
The version of NTP specified in the first selection will have to be verified it is supported by the TOE.
The cryptographic algorithms specified in the second selection of this SFR will have been specified in an FCS_COP SFR and tested in the accompanying Evaluation Activity for that SFR. Likewise the cryptographic protocol selected in the second selection of this SFR will have been specified in an FCS SFR and tested in the accompanying EA for that SFR.
The evaluator will perform the following test(s) to verify the TOE implements the selected option(s) correctly:
  Test 1: The evaluator shall configure an NTP server to use the NTP version selected by the ST Author to communicate with the NTP client – the TOE. The evaluator configures either the NTP server’s clock or the TOE’s clock such that the TOE will update its time when it receives a packet from the NTP server – the difference in time must be enough to force a step in time, and to be observable by examining the TOE’s system time before and after the event. The evaluator shall use a packet sniffer to capture the network traffic between the TOE and the NTP server. The evaluator uses the captured network traffic, the observed time change of the TOE, and the TOE’s audit log to determine that the TOE accepted the NTP server’s timestamp update and that the appropriate method and option was used to transmit the packet.
  Test 2: Check last time a valid signature packet was received by showing ….. (Mark will give it a try)

## Slide 5: Feedback – original SFR
Autokey:
There is published information on the issues using Autokey. The published information details the weaknesses in Autokey and the ease at which the timestamp data can be modified and passed along with no indication the data has been tampered.
Including Autokey as a means to authenticate the integrity of the time source provides a false sense of security that the timestamp being received is authentic and unaltered.
  Reference - https://www.ietf.org/proceedings/83/slides/slides-83-tictoc-1.pdf . In summary the paper shows that an attack can be preformed fast enough that the autokey session can be hacked in real time, crafting and sending a response well before the client times out waiting for the real (legitimate) time data.
  Reference - https://www.eecis.udel.edu/~mills/security.html where it is acknowledged "the cookie size of 4 octets is way too small"
SSH and TLS:
SSH and TLS were not included as protocols to secure the connection with the NTP server as neither support datagram protocols

## Slide 6: AAs
Guidance:
"Each primary selection in the SFR contains selections that specify a cryptographic algorithm or cryptographic protocol. For each of these secondary selections made in the ST, the guidance documentation instructs the administrator how to configure the TOE to use the chosen option(s)."
I understand that you want clear guidance instructions for each selected method. However, this overly specific language will lead to a lot of unnecessary grief for the labs. For example, rarely specifics of NTP are user-configurable. However this evaluation activity written with fully configurable implementation in mind. Instead, I recommend replacing quoted section with the following:
  "For all administrator-configurable NTP parameters, the guidance documentation must instruct the administrator how to configure the TOE and document default settings."
Test:
" a) The evaluator uses the captured network traffic, the observed time change of the TOE, and the TOE’s audit log to determine that the TOE accepted the NTP server’s timestamp update and that the appropriate option was used to transmit the packet."
“ b) The evaluator configures the TOE to secure with one of the hash algorithms and attempt to modify the timestamp to verify the TOE will reject the timestamp.”
“ c) The evaluator configures the TOE to use SHA-1 and configures the NTP server to use AES to verify the connection is not successful.”
“ d) The evaluator configures the TOE and the NTP sever to use symmetric keys to verify a successful connection and update of the timestamp.” The evaluator will modify the signature/key to verify the connection is not successful.”
“ e) The evaluator will inspect protocol handshake and confirm secure channel established, interrupt/timeout channel and make sure it is correctly renegotiated/resumed for secure channel selection.”

## Slide 7: Next Steps
Next meeting is 10:00am (EST) 28 July 2017
Finalize and approve submission to ND iTC
Provide a copy to NIAP for consideration to change PPs/EPs that include Autokey (Not a dependency for ND iTC review/approval)

## Slide 8: Thank you