## Slide 1: NTP Sub-group 21 July 2017

## Slide 2: Proposed SFR Time Stamp
Maintaining Integrity in System Date/Time
[The following is an optional SFR]
FCS_NTP_EXT.1 NTP Protocol
FCS_NTP_EXT.1.1 The TSF shall implement [selection: NTP v3 (RFC 1305), NTP v4 (RFC 5905)] NTP versions.
FCS_NTP_EXT.1.2 The TSF shall update its system time using [selection:
        Symmetric Cryptography [selection: SHA1, SHA256, SHA384, SHA512, AES-CBC-128, AES-CBC-256] as the cryptographic algorithm(s);
        The TSF shall be capable of using [selection: IPsec, DTLS] to provide trusted communication between itself and an NTP time source.
        ].
FCS_NTP_EXT.1.3 The TSF shall not update NTP timestamp from broadcast addresses.
FCS_NTP_EXT.1.4 The TSF shall support configuration of at least three (3) NTP time sources.

## Slide 3: Proposed FMT_SMF.1 SFR Update
Update to FMT_SMF.1 to include functions if NTP is selected.
    Update list of management functions that may be selected as follows:
      [selection:
          Ability to configure audit behaviour;
          Ability to configure the list of TOE-provided services available before an entity is identified and authenticated, as specified in FIA_UIA_EXT.1;
          ….
          ….
          Ability to set the time which is used for time-stamps;
          Ability to configure NTP;
          Ability to configure the reference identifier for the peer;
          ….
          ….
        ].
Update the Application Note 23 as follows:
    The TOE must provide…
    The selection “Ability…
    The selection “Ability…
    The selection “Ability to configure NTP” shall be included in the ST if the TOE uses NTP for timestamp configuration. If selected, FCS_NTP_EXT.1 shall be included in the ST as well.

## Slide 4: Proposed SFR NTP AAs
Evaluation Activities
TSS
The evaluator shall examine the TSS to ensure it describes what approach the TOE uses to ensure the timestamp it receives from an NTP time server (or NTP peer) is from an authenticated source and the integrity of the time has been maintained. The TOE may use multiple methods, as specified in the SFR, and the evaluator determines that each method selected in the ST is described in the TSS, including the algorithms and protocols used to ensure authenticity and integrity of the timestamp.
Guidance Documentation
The evaluator shall examine the guidance documentation to ensure it provides the administrator instructions on how to configure the TOE to use the method(s) that are selected in the ST. Each primary selection in the SFR contains selections that specify a cryptographic algorithm or cryptographic protocol. For each of these secondary selections made in the ST, the guidance documentation instructs the administrator how to configure the TOE to use the chosen option(s).

## Slide 5: Proposed SFR NTP AAs
Test
The version of NTP specified in the first selection will have to be verified it is supported by the TOE.
The cryptographic algorithms specified in the second selection of this SFR will have been specified in an FCS_COP SFR and tested in the accompanying Evaluation Activity for that SFR. Likewise the cryptographic protocol selected in the second selection of this SFR will have been specified in an FCS SFR and tested in the accompanying EA for that SFR.
The evaluator will perform the following test(s) to verify the TOE implements the selected option(s) correctly:
  Test 1: The evaluator shall configure an NTP server to use the NTP version selected by the ST Author to communicate with the NTP client – the TOE. The evaluator configures either the NTP server’s clock or the TOE’s clock such that the TOE will update its time when it receives a packet from the NTP server – the difference in time must be enough to force a step in time, and to be observable by examining the TOE’s system time before and after the event. The evaluator shall use a packet sniffer to capture the network traffic between the TOE and the NTP server. The evaluator uses the captured network traffic, the observed time change of the TOE, and the TOE’s audit log to determine that the TOE accepted the NTP server’s timestamp update and that the appropriate method and option was used to transmit the packet. The evaluator confirms that the TOE does not synchronize to any other time sources.
  Test 2: The Evaluator shall check last time the TOE received a valid response from its NTP server(s) or TOE peer(s) by using the ntpq utility program and issuing the 'ntpq -p' command. The evaluator shall run the test using the correct authentication credentials and re-run the test using bad authentication credentials.
  Example output format:
  remote refid st t when poll reach delay offset jitter
  ------------------------------------------------------
      *ntp.example.com .GPS. 1 u 1271 1024 367 777.176 50.073 328.874
      The TOE on which the 'ntpq -p' command was given has a remote server, ntp.example.com which is a GPL clock at stratum one (1). The 'u' under the 't' variable means unicast or manycast client. The when is the sec/min/hr since last received packet. The 'poll' is the poll interval (ln seconds). The 'reach' variable is a shift register in octal of the number of times it has received a connection to its poll request. The delay is the roundtrip delay. The offset is the offset of the server relative to the TOE. The jitter is the exponentially-weighted statistic computed by the clock discipline module. If one were to not properly configure the authentication, then one would expect to see the 'reach' variable be 0 for any measurement interval that was unable to get authenticated packets. Seeing a 3677 indication means that all packets were able to be used by the TOE.
  Test 3: The evaluator shall configure NTP servers to support periodic time updates to a broadcast address. The evaluator shall confirm the TOE is configured to not accept/receive/process broadcast NTP packets.

## Slide 6: Background Information
Autokey Consideration:
There is published information on the issues using Autokey. The published information details the weaknesses in Autokey and the ease at which the timestamp data can be modified and passed along with no indication the data has been tampered.
Including Autokey as a means to authenticate the integrity of the time source provides a false sense of security that the timestamp being received is authentic and unaltered.
  Reference - https://www.ietf.org/proceedings/83/slides/slides-83-tictoc-1.pdf . In summary the paper shows that an attack can be preformed fast enough that the autokey session can be hacked in real time, crafting and sending a response well before the client times out waiting for the real (legitimate) time data.
  Reference - https://www.eecis.udel.edu/~mills/security.html where it is acknowledged "the cookie size of 4 octets is way too small"
SSH and TLS Consideration:
SSH and TLS were not included as protocols to secure the connection with the NTP server as neither support datagram protocols

## Slide 7: Next Steps
Next meeting is 10:00am (EST) 28 July 2017
Finalize and approve submission to ND iTC
Provide a copy of the ND iTC submission to NIAP for consideration to change NIAP PPs/EPs that include Autokey (Not a dependency for ND iTC review/approval)

## Slide 8: Thank you